## Slide 1: StateMod
Maintenance Training Session #1
April 24-25, 2014

## Slide 2: Development History
Version | Year | Areas of Key Enhancements
1. | 1986 | Program developed for the Green Mountain Pump Back and Exchange Project
2. – 4. | 1995 | Baseflow module enhancement New reporting capabilities
5. | 1996 | Allow multiple replacement reservoirs Reoperate for non downstream return flows
6. | 1996 | Enhanced binary file reporting. New reporting capabilities
7. | 1997 | Treat Instream flows as a Reach Linked model capability
8. | 1998 | Daily simulation capability
9. | 1999 | Well simulation capability
10. | 2001 | Variable efficiency capability
11. | 2006 | Plan structure type added. New operating rule data that allow carrier losses, annual limits and on/off dates
12. | 2007-2008 | Irrigation Practice File is allowed to contain 4 water supply and irrigation method combinations (Expanded the ability to divert to and from plans.
13 | 2012 | Finalized plan implementation and application to South Plate

## Slide 3
Structure | Priority | Location | Demand | Ave. Eff | Immediate Return (%)
Dem_1 | 1 | Dem_1 | 2,000 af | 20 | 40
Dem_2 | 2 | Dem_2 | 3,000 af | 50 | 50
Dem_3 | 3 | Dem_3 | 1,000 af | 50 | 50
ISF_1 | 4 | ISF_1 to ISF.01 | 65 cfs | 0 (1) | 100

## Slide 4: Development Philosophy
Keep it simple
  Complexity is there if required
Help the user
  Check input data
  Backward compatible
Ability to construct input data in steps
  Stream,
  Diversions,
  Reservoirs,
  …
Simplify data input
  Quality in = quality out
  Data groups
    Structure
    Water rights
    Time series

## Slide 5
MODEL COMPONENTS

## Slide 6: Key Components
Network System
  Looks like the stream itself
Prior Appropriation Doctrine
  Modified Direct Solution Algorithm
Structure Types
  Diversion,
  Instream flows,
  Reservoirs,
  Wells,
  Plans

## Slide 7: Operating Modes
Baseflows
  Create streamflow without man’s impact
  100% is natural, <100% is baseflow
Simulate
  Calibrate to history
  Simulate future conditions
Report
  Standard reports
  Detailed as needed
Data check
  Verify input data

## Slide 8: Baseflow
Create streamflow without man’s impact
  100% is natural, <100% is baseflow
Can operate with missing data
100% Removed is Natural flow

## Slide 9: Gaged Baseflow
Gaged (Qg) = Qg + D – R – S + E
Baseflow Calculation |  |  | 
Item | Ex 1 | Ex 2 | Ex 3
Gaged | 1,000 | 1,000 | 1,000
Diversion (-) | 500 | 500 | 500
Return Flow (-) | 200 | 0 | 400
Storage Increase (-) | 210 | -490 | 1490
Evaporation Loss (+) | 10 | 10 | 10
Baseflow | 1,100 | 2,000 | -380

## Slide 10: Un-gaged Baseflow
FlowX = gaged portion + ungaged portion
  Gaged = (FlowB(1)*coefB(1) + FlowB(2)*coefB(2)+ ....)
  Ungaged = pf * (FlowG(1)*coefG(1) + FlowG(2)*coefG(2)+ ..
FlowX = 1,000*1.0 + 3,000*1.0 + 0.70*(6,000*1 – 1,000*1-3000*1)

## Slide 11: Simulate (Stream Allocation)
Water availability is determined for network
The most senior water right is identified
Allocate diversion using the MDSA
  Min (available flow, demand, water right, capacity, other)
Downstream flows are adjusted
Return flows for future time periods are stored
Well depletions for future time periods are stored
Check for need to need to reoperate
  If yes, go back to step 2 and repeat with the most senior water right
Repeated by priority for each successive direct, instream, storage, well and operational water right.
The process is repeated for each month or day of the study period

## Slide 12: Report
Standard
  Network *.xdd
  Diversion & well *.xss
  Reservoir output: *.xre
  Well output: *.xwe
  Plan output: *.xpl
  Operating Rule Info: *.xop
  Instream Reach Info: *.xir
  Structure Summary: *.xss
  Call (Control) Summary: *.xca
Detailed
  Water Balance *.xwb
  Diversion comparison *.xdc
  CU summary *.xcu
  …

## Slide 13: Data Check
Read input data
Standard Reports
  Base flow (*.xbc)
    Compare gaged to ungaged flow
  Direct demand (*.xcd)
  Instream Demand (*.xci)
  Well Demand (*.xcw)
  Water Right List (*.xwr)
  Output Request (*.xou)

## Slide 14
FEATURES

## Slide 15: Features
Modified Direct Solution Algorithm MDSA)
  Include immediate return flows w/o iteration
  Reoperates if new water is added to system
Daily or Monthly
Variable efficiency
Soil accounting
Wells
Plans
Operating rules

## Slide 16: Modified Direct Solution Algorithm
In summary:
  Direct Solution Algorithm (see handout):
    For every node downstream:
    Divert = min(demand, water right, capacity, available flow
    If available flow limits:
    Divert = Available Flow / (1.00-efficiency) * (return (0))
  Modified Direct Solution Algorithm (see handout)
  Allow variable efficiency and soil accounting
    Requires Consumptive Water Requirement (CIR) data
    Requires maximum efficiency data

## Slide 17: Reoperation
Check for new water
  Reservoir releases
  Non downstream returns
Reoperate
  Determine if a senior right
    can benefit from new water
    by repeating the water
    right loop
Control
  Off (testing)
  On (simulate)
  Reoperate when the sum of reservoir releases and non-downstream return flows exceed a specified value

## Slide 18: Daily Operations
Build upon a monthly model
  System understanding
Daily input options
  Provide daily data for only those component where it is necessary or justified (e.g. streamflow but not reservoir targets)
Options
  Daily data provided
  Use a monthly average
  Similar to another station
  Connect monthly midpoints (demand)
  Connect monthly end points (reservoir target)
No routing

## Slide 19: Variable Efficiency
Major component to MDSA
Allows the efficiency of water use to vary from 0 to a maximum.
Soil moisture accounting may be included
Does not apply to reservoir releases
Data requirements
  Consumptive water requirement
  Maximum efficiency
    Sprinkler or
    Flood

## Slide 20: Soil Accounting
Requires the variable efficiency option
Capacity = depth * area * capacity
Max diversion to storage is the minimum of soil capacity and diversion * efficiency
If area is reduced in a time step and soil capacity is exceeded the difference is a loss
Amount to Storage for various maximum efficiency values |  |  | 
Given: Storage Capacity | 200 |  | 
Item | Ex 1 | Ex 2 | Ex 3
Divert | 1000 | 1000 | 1000
Max efficiency | 40% | 60% | 70%
CIR | 500 | 500 | 500
CU | 400 | 500 | 500
Final soil storage | 0 | 100 | 200

## Slide 21: Wells
May be independent or tied to a diversion
Do not need to be in network
Demands
  If independent, they are provided in the well demand file
  If tied to a diversion, provided as a well demand (calibration) or as part of a diversion demand (simulate)
Well operations can cause the system to reoperate
If depletions exceed streamflow
  Water is taken from groundwater storage
  Groundwater storage is paid back in next time step
Can be tied to augmentation plans
Reported in two pieces:
  From well (pumping this time step) and
  Well Depletion (prior pumping)

## Slide 22: Plans
Originated for wells
Expanded to include many complex features (see section 3.9 of documentation for descriptions)
  Accounting
  Reservoir reuse
  Non reservoir reuse
  Transmountain imports
  Terms and conditions
  Well augmentation
  Recharge plan
  Out of priority diversions
  Release limit
  Special well augmentation (designated basin, coffin wells, etc)

## Slide 23: Operating Rules
Allow complex owner and water rights to be simulated
Began with 12 and have grown to 50
  See section 4.13 of documentation
In general must know 3 things
  Source of Water
    Water right, reservoir, well, water right , plan
  Destination of water
    Diversion, reservoir, well, instream flow or plan
  Delivery method
    Stream or carrier
    With or without losses
Special operating rules
  Compacts, soil moisture, storage

## Slide 24: Soil Accounting
Requires the variable efficiency option
Capacity = depth * area * capacity
Max diversion to storage is the minimum of soil capacity and diversion * efficiency
  Water use efficiency includes soil storage
If area is reduced in a time step and soil capacity is exceeded the difference is a loss
Amount to Storage for various maximum efficiency values |  |  | 
Given: Storage Capacity | 200 |  | 
Item | Ex 1 | Ex 2 | Ex 3
Divert | 1000 | 1000 | 1000
Max efficiency | 40% | 60% | 70%
CIR | 500 | 500 | 500
CU | 400 | 500 | 500
Final soil storage | 0 | 100 | 200

## Slide 25: Water Balance
Stream Inflow
  Return
  To/From GW Storage
  Total In
Stream Outflow
  From river by well
  Well Depletion
  Reservoir Evaporatoin
  Stream Output
  Total Out
Delta (In – Out)
Other
  CU
  Loss
  Pumping
  Salvage

## Slide 26: Documentation
Acknowledgment
Introduction
Model description
Input data
Output data
Model operation
Technical notes
  Describes various technical issues
Frequently asked questions
Supporting utilities
Discontinued but supported files