## Slide 1: StateMod Program Description
Maintenance Training Session #1
April 24-25, 2014

## Slide 2: Programming Philosophy (1/2)
Help the user
  Input data units
  Input data detail (average, monthly, daily)
Backward compatible
  Support old data formats
Check input for reasonableness
  Catch for potential problems before trying to simulate
  Particularly for operating rules
Detailed checking
  Control variable (ichk) offers over 25 options
Allow major control (on/off) without revising input
  Control variables for wells, variable efficiency, time period, output units

## Slide 3: Programming Philosophy (2/2)
Minimize memory requirement
  Read time series once per year
  Print output to a binary file every time step
Maximize local variables
  Initialize data to scalars every time step
    Dem = Demand(I,j)
Performance is critical
Help user/programmer find problems
Once water is allocated, do not take away

## Slide 4: Memory
Two files of common block data
  Common.inc
    All common blocks except daily
  Daily.inc
    Daily data only
Subroutine StateM
  Contains current limits of model
  Used unique values to allow easy replacement

## Slide 5: Typical Operating Rule Structure (1/2) (see DivcarL)
Three components prior to code:
Program description
  DivcarL; It simulates a type 45 operating rule for carrier structures with Losses
Update History
  rrb 2007/04/16 Revised to allow various owners to share in water supply and capacity
Documentation
  CallBy calling routine
  IW Overall water right order
  L2 Location of operation right in opr right table

## Slide 6: Typical Operating Rule Structure (2/2) (see DivcarL)
Code identifies steps associated with key steps
  Step 1 Initialize
  Step 2 Exit if not on this month
  Step 3 Set Source data
Detailed Output
  Allows detailed results if requested

## Slide 7: Flow Charts
Main see Statem
Baseflow see Virgin
Simulate see Execut
Report see Report
Data check see Xdebug

## Slide 8: Other (1/2)
Database of input
  Easier maintenance
Memory limits
  Western slope was near limit of old compilers
Operating rule redundancy
  Backward compatibility
Documentation
  Always room for improvement
Daily return flows
  If day 1 = 0, performance can be significantly improved

## Slide 9: Other (2/2)
Calibration in steps
  Run in a monthly time step
  Begin with stream and diversions
  Add reservoirs, wells, plans, …
Baseflows
  Understand why negative base flows may occur
  Eliminate them if possible
Simulate
  Limit degrees of freedom
    Fix demand and reservoir data
      Verify water right and operating rule operations
    Sequentially free reservoirs & demands
  Check
    Monitor to/from ground water storage
    Monitor water balance
    Review output